## Slide 1
Capacitors
Scale in cm
An electrical component which stores charge
parallel plate capacitor

## Slide 2
Leyden Jars
It was invented independently by German cleric Ewald Georg von Kleist on 11 October 1745 and by Dutch scientist Pieter van Musschenbroek of Leiden (Leyden) in
1745–1746.

## Slide 4
Parallel plate capacitor

## Slide 5
A dielectric increases the charge on the plates

## Slide 6
  Capacitors in a parallel configuration each have the same applied voltage. The total charge stored is therefore
Capacitance is measured in Farads
1F means one coulomb per unit volt between the capacitor plates.
A Leyden Jar has a capacitance of around 1 nF. A typical circuit board capacitor will have capacitance from a few pF up to a large number of mF
Since the total capacitance is given by
Therefore parallel capacitances add

## Slide 7
Sum of voltage drops across capacitors must equate to the applied voltage
Hence:
Now the charge on each adjacent capacitor plate must be the same, otherwise current
would flow between the capacitors, re-apportioning charge
Hence:
Therefore the reciprocals of series capacitances add

## Slide 8
Capacitance examples

## Slide 9
Energy stored in a capacitor
The instantaneous power required to establish voltage V across the plates
of a capacitor is
In time interval dt, the amount of charge added to the capacitor is
Hence current I is
Total energy required to establish voltage
V across the capacitor plates (in time t)
is therefore

## Slide 10
The capacitance of a metal sphere of
radius R is given by
The permittivity of free space is
So the Capacitance of a 0.2m radius
Van der Graaf generator is about 22pF
The energy stored in a capacitor is
The voltage of a typical Van der Graaf might be as high as 300kV
Hence the energy discharged is only about 1J and the charge about 6.6mC
Reference

## Slide 11
Capacitors, combined with other basic components such as resistors and inductors can form a huge variety of circuits, each with a different application.
An integrated circuit (on a ‘chip’) is the basis of modern electronics. A computer microprocessor may contain billions of circuits!
This particular circuit
generates a sine wave
oscillating signal at a frequency dependent upon the parameters of the components i.e. capacitance, inductance etc

## Slide 12
Charging a capacitor using a DC source
Switch
1. Switch closed. Current flows through
resistor and positive charge builds up
on right capacitor plate. An equal amount of
negative charge builds up on left plate.
2. Electrical field set up between capacitor
plates as no current can flow. Voltage V between
the plates is V = Q/C where Q is the total charge
deposited and C is the capacitance (‘charge per unit volt’)
3. As charge builds up on right plate, potential
difference between capacitor and source reduces.
This reduces the current flowing onto the plate.
Eventually the voltage V becomes V0 and hence no more current can flow.
3. Note the amount of charge which can be deposited depends on the resulting electrical field strength between the plates. Above the breakdown field strength, current will flow between the plates
Dielectric | Breakdown field strength /Vm-1
Air | 3 x 106
Mineral oil | 15 x 106
Neoprene | 16 x 106
Water | 65 x 106
Mica | 118 x 106

## Slide 13
Charging a capacitor using a DC source
capacitor charge, voltage relationship
Ohm’s law
Definition of current

## Slide 14
Discharging a capacitor
capacitor charge, voltage relationship
Ohm’s law
Definition of current, and negative since charge is discharged from plates
Note V=V0 when t = 0
So RC is a characteristic time for
charging or discharging a capacitor