## Slide 1: via the Fine Beam Tube
A. French. February 2017

## Slide 2
Calculating the electron charge to mass ratio using a Fine Beam Tube
This experiment refers to the Fine Beam Tube model
number 555 58 Baur 2 made by Leybold.
https://www.leybold-shop.co.uk/
‘Actual’ values
Low pressure hydrogen gas inside a spherical tube is ionized by a beam of electrons, which are accelerated via a voltage of approximately 100V. A pair of Helmholtz coils (solenoids) produce a highly uniform magnetic field which bends the beam into a circle.
If the accelerating voltage, the coil current and the beam radius are measured, it is possible to calculate from these parameters the electron charge to mass ratio
Electron beam
Cathode
Anode
6.3VAC heater, to generate free electrons, which
are then accelerated by a DC potential

## Slide 3
Assume uniform magnetic field of strength B between the Helmholtz coils.
The force on an electron (beyond cathode and deflection plates) is
i.e. a purely centripetal force if the beam is initially
vertical and perpendicular to the uniform
magnetic field.
Newton II (+ve in radially inward direction):
Electron
Assume electron kinetic energy is solely from the accelerating potential, and velocities
are low enough such that relativistic effects can be ignored.*
* See next page!
Hence:
The charge to mass ratio for an electron can
therefore be determined in terms of readily measurable quantities via the Fine Beam Tube!

## Slide 4
Classical result:
So the Fine Beam tube can be used to measure the electron charge to mass ratio by plotting a graph of y vs x and finding the gradient.
1
I = 0.744A r = 0.0569m
For a pair of Helmholtz coils with N turns and radius R
separated by distance 2h, the magnetic field strength
along the coil centre line, half way between the coils, is:
Magnetic field
on axis from a current loop of N turns
Permeability of free space

## Slide 5
Do we need to account for relativistic effects?
Define ‘Relativistic’ if:
Classical energy formula
‘Actual’ values
So since our accelerating potentials are about
180V, we might find the effects are small.
However, if v/c = 0.01, the ‘relativistic voltage’
becomes 25.6V.
So we might expect relativistic effects to be
small but perhaps not insignificant.

## Slide 6
Assume centripetal acceleration
Relativistic effects
Newton II:
Relativistic Kinetic Energy
equated to accelerating
potential multiplied by the
electron charge
Newton II applied radially:

## Slide 7
Classical result
Relativistic result
Define percentage increase due to relativistic effects:

## Slide 8
For the range of voltages
we will be using, we anticipate
the % change in beam radius
to be negligible i.e. of the order
of about 0.01%
If on the other hand we use an accelerating potential of a few million volts (or much higher, as they do in particle accelerator experiments) we would notice a significant difference between classical and relativistic results.

## Slide 9
What about the effect of the electron beam being at radius r from the central axis
between the Helmholtz coils? Let’s firstly consider a ‘single loop’ of N tight coils of radius R:
Biot-Savart law
Define a numerical method to compute the x,y,z components of the magnetic field.
Evaluate at
Since the second solenoid
is identical and equidistant
we can simply multiply
the magnetic field
by two.
e.g. P = 1000
Given the ‘cylindrical symmetry’
of the system, this is a quite
general result

## Slide 10
The off-axis magnetic field strength is evaluated as a function of radius r from the centre
of the Fine Beam Tube. For the range of measured r values, the degradation from on-axis
field strength is a maximum of about 2%.
On axis field strength
at r = 0 is:
The field strength
only significantly
drops when the radius is greater than about 8cm.
So since the tube
has an 8cm radius
we expect the magnetic field to be essentially uniform.

## Slide 11
Assembly & storage
170V DC
(& 6.3V AC)
power supply
Variable resistor
(in box with tube)
Fine beam tube + Helmholtz coils

## Slide 12
Helmholtz coils
Radius R = 0.15m
N = 130 turns
Coil separation
2h = 0.15m
Fine beam tube
0.08m radius filled with Hydrogen
gas, pressure about
1Pa
Power supply for Helmholtz coils
(about 6V DC)
Potentiometer to vary current through coils
Coil voltmeter
Coil ammeter
Voltmeter
for ES deflection plates
Potentiometer
to control ES deflection
plate voltage
6.3VAC heater
supply
160-180V DC
power supply
to accelerate electrons
Experimental setup

## Slide 13
Cathode
Electron deflection plates
Anode
Helmholtz coil power supply & potentiometer. Current should be between 0.6 and 1.5 amps
Fine beam tube power connectors
Electron beam
Top layer of 130 turn Helmholtz coil
(note there are layers below)

## Slide 14
Switch on the heater circuit (max 6.3VAC) for about a minute before
connecting up the 180V DC accelerating voltage
Checking the
supply voltage
before wiring up the
Fine Beam Tube

## Slide 15
(Spherical) tube radius a = 0.08m
Helmholtz coil radius R = 0.15m
Coil separation 2h= 0.15m
Number of turns per coil N = 130
Fine beam tube dimensions
a = 0.08m
2h= 0.15m
R = 0.15m

## Slide 16
Too much ES deflection will divert the electron beam off centre
Setup problems – and how to correct them

## Slide 17
If the electron beam is not pointing straight up, the magnetic field will cause the beam to spiral
into a helix. Correct this by gently rotating the tube. The goal is to achieve a circular beam
centred on the longitudinal axis between the Helmholtz coils – i.e. where the magnetic field
is most uniform and readily calculable!
Setup problems – and how to correct them

## Slide 18
Holding a neodynium magnet close to the tube will result an impressive helical beam.
CAUTION hold the magnet with care – if it slips from your hand towards the metal
parts of the tube it could potentially cause significant damage. At very least use a magnet
covered in plastic.

## Slide 19
To see the electron beam (which causes ionization of the low pressure Hydrogen, which in turn releases blue/purple frequency light) you will need to have very low light levels
in the laboratory.
To photograph the beam, set up a camera on a tripod inside a black ‘tent’ made from the black towel which comes with the kit.
All the images in this presentation were shot using a Panasonic Lumix TZ8 in ‘Starry Night’ mode with a 60s exposure. To reduce camera shake and initial lighting, use a 10s delay. This should be ample time to cover the equipment with the black cloth and turn off the laboratory lights!
Notice the beam often has
a significant spread. This is because there is likely to be a spectrum of energies for the accelerated electrons, with mean eV,
where V is the accelerating potential
Electron
beam
Cathode

## Slide 20
01 I = 0.689A r = 0.0594m
02 I = 1.270A r = 0.0339m
03 I = 1.108A r = 0.0400m
04 I = 1.045A r = 0.0424m
05 I = 0.997A r = 0.0448m
06 I = 0.947A r = 0.0469m
07 I = 0.905A r = 0.0490m
08 I = 0.845A r = 0.0528m
09 I = 0.793A r = 0.0551m
10 I = 0.744A r = 0.0569m
11 I = 0.700A r = 0.0593m
12 I = 0.657A r = 0.0588m
13 I = 0.882A r = 0.0497m
14 I = 1.151A r = 0.0358m
Using a potentiometer to vary the
Helmholtz coil current, and hence magnetic field strength, and therefore the beam radius
NOTE: Power supply and variable resistor settings for ES
deflection were unmodified. However, the voltage across the power supply was observed to change slightly (between 169 and 176V DC).
The power supply voltage was recorded for each of the fourteen experiments, and this variable result was used in the calculations.

## Slide 21
Experiment # 07
14.9
min diameter
= 8.43cm
max diameter
= 9.82cm
Using PowerPoint to measure beam radius r
PowerPoint scale
Overlay circles
in PowerPoint
Calculate minimum and maximum circle radii,
noting radius of tube is 0.08m

## Slide 22
Beam radius is taken as the
mean average of the max and min
measured radii. The error is defined
as half the difference between these radii.
Errors in voltage and current
measurements were inferred
by eye from the fluctuations
in the multimeter readings.
Error boxes correspond to the full range of possible values (i.e. upper and lower bounds) given the stated errors.

## Slide 23
With ‘0.57 fudge factor’
i.e. assume the accelerating
potential V is actually 57%
of the voltage across the power
supply.
This is proposed as the most obvious
source of discrepancy between
the measured and predicted
lines.

## Slide 24
With ‘0.595 fudge factor’
i.e. assume the accelerating
potential V is actually 59.5%
of the voltage across the power supply.
This is proposed as the most obvious source of discrepancy between
the measured and predicted
lines.
The ratio of the
measured to actual
e/m value is:
1.76/2.96 = 0.595

## Slide 25
Summary
indeed yields a fairly straight line with significant correlation, although the measured gradient of 2.96 x 1011 C/kg differs quite significantly from the predicted value of 1.76 x 1011 C/kg.
The most likely source of error is that the actual accelerating voltage is much less than the measured voltage across the terminals. i.e. there is a significant internal resistance.
Off-axis magnetic field degradation or Relativistic effects are not thought to be as important.
Multiplying the measured e/m by 0.595 results in the actual value, i.e. an
expected voltage loss of 40.5%. Note a loss factor (‘fudge factor’!) of 0.57 actually gives a slightly
better agreement of the measured data with the predicted line, although the gradient differs slightly from the predicted e/m value.
The beam was rarely thin, indicating a range of electron energies at the point of emission. This might augment the ‘internal resistance’ hypothesis for a modification of V, although this effects is reflected in
the error bars.
Further investigation:
Change the power supply, perhaps using a higher voltage (up to perhaps 250V). Do x,y
values lie on the same line as in this experiment? Is the voltage loss systematic?
Find some mechanism for directly measuring the accelerating potential. Can the anticipated 40.5% loss
be calculated independently?
Note Leybold have upgraded the equipment over the years. Perhaps the internal resistance / spectrum
of electron energies issue has been fixed? It might be worth contacting Leybold directly.

## Slide 26
To be continued!